## Slide 1: DMZ Virtualization Phase 1
Hardware/Licensing Requirements:
  REPURPOSE: 2 IBM Utility Servers and Arrow Server to Virtual Network
  NEED: 2-port 10GBE Interface Cards to each server
  NEED: 2-16 Port GBE Switches
  NEED: 30TB SAN
  NEED: VMWare Licensing for each CPU Socket on IBM Servers
Connectivity/Security
  SAN and Servers are connected via 10GBE switch with ISCSI interfaces. The SAN will sit on a private network with no connectivity to the Virtual Machines hosting applications
  Use existing FW and switches with virtual vSphere® Distributed Switch (VDS) to conform to existing DMZ zoning and security requirements
Migrate ANLP, DDOS, MSD and FLSTG to the Virtual Environment
Verify applications and run testing to verify Virtual Environment, e.g., HW failures, cable pulls

## Slide 2
FDC Egress Firewalls 01ca/02ca
Shadownet Access from
Middletown
Secaucus
Bridgeton
UGN Access
DMZ1 Zone
DMZ2 Zone
UGN VLAN
UGN Zone
Shadownet Zone
FDC VLAN
FDC Egress Switch
Inside Zone
MED
(2) IBM
3650
30TB SAN
IBM
3650
IBM
3650
IBM
3650
FDC Access
10GBE
VLAN Trunk *
VLAN Trunk *
ISCSI
ISCSI
IMM VLAN
DATA VLAN
OAM VLAN
IMM VLAN
DATA VLAN
OAM VLAN
10GBE
Architecture
Phase 1
VDS 4
SAN
VDS 3
OAM
OAM
VDS 1
DMZ ZN1
IMM
DATA
VDS 2
DMZ ZN2
IMM
DATA
Windows
Server
ESXi
Hypervisor
DDOS
MSD
ANLP
FLSTG

## Slide 3: DMZ Virtualization Phase 2
Migrate the 4 Servers formerly hosting (ANLP, DDOS, MSD and FLSTG) to the Virtual Environment
Migrate SECAUCS (Datacache, Application, Web) Server to the DMZ Virtual Environment. IGW is optional and can be moved later if security/connectivity requirements can be satisfied in the DMZ
Migrate Collaboration Portal to the DMZ Virtual Environment

## Slide 4
IBM
3650
IBM
3650
IBM
3650
IBM
3650
FDC Egress Firewalls 01ca/02ca
Shadownet Access from
Middletown
Secaucus
Bridgeton
UGN Access
DMZ1 Zone
DMZ2 Zone
UGN VLAN
UGN Zone
Shadownet Zone
FDC VLAN
FDC Egress Switch
Inside Zone
MED
(2) IBM
3650
30TB SAN
IBM
3650
IBM
3650
IBM
3650
FDC Access
VDS 4
SAN
10GBE
VDS 3
OAM
OAM
VLAN Trunk *
VLAN Trunk *
ISCSI
ISCSI
IMM VLAN
DATA VLAN
OAM VLAN
IMM VLAN
DATA VLAN
OAM VLAN
10GBE
Architecture
Phase 2
VDS 1
DMZ ZN1
IMM
DATA
VDS 2
DMZ ZN2
IMM
DATA
Windows
Server
ESXi
Hypervisor
DDOS
MSD
ANLP
SECS
SECS
SECAUCS
SECS
SECS
CLBP
FLSTG